# Text boxes

Ziya Gökalp Mah. İkitelli Organize Sanayi Bölgesi Atatürk Bulvarı No:50 34490 Başakşehir / İstanbul / TÜRKİYE

Telefon : +90 212 549 22 52

Faks      : +90 212 549 25 80

Web      : www.emasas.com.tr

EMAS ELEKTROTEKNİK MAKİNA    SANAYİ VE TİCARET A.Ş

Technical Specifications : L52K13MUM331

Order Code:

L52K13MUM331

Contact Block:

1NO + 1NC

Snap action

Finger protection terminals

Screw washer

Electrical insulated

Snap action

Technical Information :

| Body: |
| --- |
| Prismatic metallic housing and cover |
| PG13,5 cable entry |
| General Specifications |  |
| Operating Temparature | -5/+40°C |
| Mechanical life | 10 Million (3000 open-close/hour |
| Electrical Life | 1 Million (1800 open-close/hour) |
| C.Block Tightening Torque | 0,6-0,8 Nm |
| C.Block Connection Wire Profile | Min: 1x0,5 mm'2 |
| Wire Profile | Max: 2x2,5 mm'2 |
| Protection Degree | IP65 |

Electrical Informations :

Standards:

- TS EN 60947 -5-1

In contact Blocks;

- VDE 0660

-  UL 508

| General Specifications |  |  |
| --- | --- | --- |
| Range Of Use |  | AC15 |
| Operating Voltage | Ue | 240V AC |
| Fregquency | f | 50Hz |
| Operating Current | Ie | 3A |
| Insulation Resistance Voltage | Ui | 500V |
| Stroke Resistance Voltage | Uimp | 6kV |
| Dielectrical Strength |  | 1500V AC |

Electrical Informations :

| General Specifications |  |  |
| --- | --- | --- |
| Range Of Use |  | AC15 |
| Operating Voltage | Ue | 230V AC |
| Fregquency | F | 50Hz |
| Operating Current | Ie | 4A |
| Insulation Resistance | Ui | 300V |
| Stroke Resistance Voltage | Uimp | 2.5kV |
| Dielectrical Strength |  | 1500V AC |